DT-ENG-608-V1 / 201708

2 WIRE SYSTEM

DT608 Series

Fisheye door station with proximity access control

USER MANUAL

RF CARD

DT608/ID/FE-S8

EP608-S12

DT60C-S8

·  Please read this manual carefully to ensure safe and correct operation.

·  Keep this manual well for future reference.

CONTENTS

PARTS AND FUNCTIONS ..................................................................................... 3

Part Names............................................................................................................. 3

Mounting................................................................................................................. 3

Terminal Description ............................................................................................... 4

BASIC FUNCTIONS .............................................................................................. 5

Unlock Operations .................................................................................................. 5

Fisheye Camera ..................................................................................................... 5

External Motion Detection ...................................................................................... 5

SETUP INSTRUCTIONS........................................................................................ 6

Functions Setting Up .............................................................................................. 6

Setting Door Station Address ................................................................................. 7

Setting Door Station Calling Mode ......................................................................... 7

Setting Camera N/P Standard ................................................................................ 9

Setting Prompt Voice .............................................................................................. 9

Setting Prompt Voice Volume ................................................................................ 10

Setting Unlock Mode ............................................................................................. 10

Setting Unlock Time............................................................................................... 11

Setting Nameplate Illumination Mode.................................................................... 11

Setting Night View LED Illumination Mode ............................................................ 12

Setting Ring-back Tone ......................................................................................... 12

Setting Image Display Mode.................................................................................. 13

RAINY_COVER Configure .................................................................................... 14

Registering ID Card ............................................................................................... 15

Restore To Default................................................................................................. 17

WIRING ................................................................................................................. 18

Connecting Electric Lock ....................................................................................... 18

As The Villa System Door Stations........................................................................ 19

As The Apartment System Door Stations .............................................................. 20

APPENDIX ............................................................................................................ 21

Precautions............................................................................................................ 21

Specification .......................................................................................................... 21

Cables and Requirments ....................................................................................... 22

PARTS AND FUNCTIONS

Part Names

[9]

[10]

[8]

[1]

[2]

[11]

[7]

[3]

[6]

[4]

[12]

[5]

[1] Microphone

[2] UNLOCK indicator

[3] CALL indicator

[4] Call button

[5] Nameplate

[6] Speaker

[7] Night view LED

[8] Camera lens

[9] Rainy cover

[10] Mounting hook

[11] Connection port

[12] External key module

Mounting

The installation height is suggested to 145~160cm.

1

2

Rainy cover

Main unit

The distance between

the top of main unit

and rain cover should

be not less than 3mm.

≥3mm

3

4

5

Rainy cover

Main unit

AcDbMLeader(ACDB_MLEADER_CLASS)

AcDbMLeader(ACDB_MLEADER_CLASS)

AcDbMLeader(ACDB_MLEADER_CLASS)

AcDbMLeader(ACDB_MLEADER_CLASS)

1. Drill holes in the wall to match the size of screw stoppers, then attach the rainy cover to the

wall.

2. Connect the cable correctly, and attach the main unit to the rainy cover. The distance between

the top of main unit and rain cover should be not less than 3mm.

-3-

PARTS AND FUNCTIONS

3. Install the name plate.

4. Attach the front panel to the rainy cover.

5. Use the special screwdriver and the screws to fix the panel.

Terminal Description

Lock Control Jumper

1 2 3

3P Connect Port

L1 L2

PL S+

S-

Main Connect Port

Lock Control Jumper: To select the lock type.

3P Connect Port: 1. If the external key module is detected online, the port will be

automatically as a communication port;

2. If there is no the external key module, it will check whether the PIR function is enabled. If the

PIR function is enabled, it will be as the detection port of the PIR;

3. If above cases are not activated, GND and PIR can be used as exit button port.

Main Connect Port: To connect the bus line and the electronic locks.

· L1,L2: Connect to the bus line, no polarity.

· PL: External lock power input, connect to the power positive(power +).

· S+: Lock power(+) output.

· S-: Lock power(-) output, connect to the power(-) input of locks(only when using the door

station to power the locks, if using the external power supply for the locks, the S- will not be

connected).

-4-+12V

GND

PIR

BASIC FUNCTIONS

Unlock Operations

Unlocking of ID Card

When the registered user card has been shown to ID card window, the UNLOCK indicator lights

up, the buzzer sounds,and the electric door strike is unlocked.

· If show the authorized user card,the buzzer will sound of beep+,and the UNLOCK indicator

will light up.

· If show the unauthorized user card,the buzzer will sound of beep,beep,beep.

Fisheye Camera

Please note that this function requires the

monitor with fisheye function to support.

The angle view is 1700,visitors in this angle

view can be seen clearly and can be zoomed

to see individuals up close via indoor monitor

with fisheye function.

External Motion Detection

The door station is equipped with a terminal to

connect external motion detector.

If the external motion detector is connected

to the system,following functions will be effec-

tive:

If detect someone passing by, the door station

can be activated operation to unlock or turn

12V

GND

PIR

Standard

door station angle

DT608

1700 door camera angle

(Wide angle view shown)

Motion

detector

on light.

* Please contact with supplier for more details about

detector connection.

-5-

SETUP INSTRUCTIONS

Functions Setting Up

This section explains the settings of each

function, please refer to the following table:

To perform the settings for the function

you want,you should move away the metal

front panel. Please refer to the sketch

map.

Each operation is indicated by the lighting

up of the LED indicator on the unit, and by

LED_NAME

RF CARD

LED_UNLOCK

LED_CALL

KEY_SET

KEY_4

KEY_3

KEY_2

KEY_1

the sounding of the buzzer.

Main unit

| -6-Order | Setting items | Setting range | Default value |
| --- | --- | --- | --- |
| 1 | Setting door station address | 0~3 | 0 |
| 2 | Setting door station calling mode | Standard/Group calling mode | Standard calling mode |
| 3 | Setting camera N/P standard | N/P standard | P standard |
| 4 | Setting prompt voice | Max. 9 voices | Voice 1 |
| 5 | Setting prompt voice volume | 1~9 | 6 |
| 6 | Setting the unlock mode | 0:opened/1:closed | 0:opened |
| 7 | Setting the unlock time | 01 to 99 seconds | 1 seconds |
| 8 | Setting the nameplate illumination mode | On/Off/Auto | On |
| 9 | Setting night view LED illumination mode | On/Off/Auto | Auto |
| 10 | Setting ring-back tone | Ringing one time Ring continuously No ring-back tone | Ringing one time |
| 11 | Setting image display mode | Alternate switching mode Zoom mode Full screen mode | Alternate switching mode |
| 12 | RAINY_COVER configure | Provide / not | Provide |

SETUP INSTRUCTIONS

Setting Door Station Address

Total 4 addresses can be configured. It can be modified either before or after installation.

0 is default, to change the setting, please follow the steps:

ID=0,1st door station

ID=1,2nd door station

ID=2,3rd door station

ID=3,4th door station

In standby mode, press

KEY_SET button once

UNLOCK Indicator:OFF

TALK Indicator:OFF

Buzzer

Beep+, Beep

Press KEY_1 button to set

the first door station.

UNLOCK Indicator:OFF

TALK Indicator:OFF

Press KEY_2 button to set

the second door station.

UNLOCK Indicator:OFF

TALK Indicator:OFF

Press KEY_3 button to set

the third door station.

UNLOCK Indicator:OFF

TALK Indicator:OFF

Press KEY_4 button to set

the fourth door station.

UNLOCK Indicator:OFF

TALK Indicator:OFF

Buzzer

Beep+

Buzzer

Beep,Beep

Buzzer

Beep,Beep,Beep

Buzzer

Beep,Beep,Beep,Beep

· If setting mode has not been exited, you can change the address of door station by pressing KEY1~4

freely.

· The LED_NAME indicator will always blink until exit out the setting mode.

· If without any operation in 10 seconds, it will exit out setting mode automatically.

· In this step,press KEY_SET button four times to exit out the setting mode manually.

Setting Door Station Calling Mode

There are two calling modes for door station.

As apartment system door station, the calling mode is Standard calling mode.

As villa system door station, the calling mode is Group calling mode.

Please know that the door station work in Standard calling mode by default.

-7-

SETUP INSTRUCTIONS

Each call button will respond different addresses when set in different calling mode. Refer to the

followings for more informations.

1.Standard calling mode(Address range 01-08 by

default)

RF CARD

Apartment system

door station

RF CARD

H

G

F

E

D

C

B

A

B

A

Call buttonA: call the monitor with address 01 by default.

Call buttonB: call the monitor with address 02 by default.

Call buttonC: call the monitor with address 03 by default.

Call buttonD: call the monitor with address 04 by default.

Call buttonE: call the monitor with address 05 by default.

Call buttonF: call the monitor with address 06 by default.

Call buttonG: call the monitor with address 07 by default.

Call buttonH: call the monitor with address 08 by default.

2.Group calling mode

Call buttonA: Call all monitors in group address from

00~15.(one of the monitor should be set to 00)

Call buttonB,C,D,E,F,G,H: Call all monitors in group

address from 16~31. (one of the monitor should be set to

Villa system door station

16)

* More details about code setting for monitor, please refer to corresponding user manual .

To change this setting, please follow the steps:

In standby mode, press

KEY_SET button twice.

UNLOCK Indicator:OFF

CALL Indicator:ON

Press KEY_1 button to

activate Standard calling

mode for door station.

UNLOCK Indicator:OFF

CALL Indicator:ON

Press KEY_1 button again

to activate Group calling

mode for door station.

UNLOCK Indicator:OFF

CALL Indicator:ON

Buzzer

Beep+, Beep

Buzzer

Beep+

Buzzer

Beep, Beep

Press KEY_1

· If setting mode has not been exited, you can change the calling mode by pressing KEY1 circularly.

· The LED_NAME indicator will blink all the time until exit out the setting mode.

· If without any operation in 10 seconds, it will exit out setting mode automatically.

· In this step,press KEY_SET button three times to exit out the setting mode manually.

-8-

SETUP INSTRUCTIONS

Setting Camera N/P Standard

The standard of the camera can be adjusted at any time, that means the quality of image on

screen can be set to differ.

P standard is default, to change the setting, please follow the steps:

In standby mode, press

KEY_SET button twice.

UNLOCK Indicator:OFF

CALL Indicator:ON

Press KEY_2 button to set the

camera standard to P

standard.

UNLOCK Indicator:OFF

CALL Indicator:ON

Press KEY_2 button again

to set the camera standard

to N standard.

UNLOCK Indicator:OFF

CALL Indicator:ON

Buzzer

Beep+, Beep

Buzzer

Beep+

Buzzer

Beep, Beep

Press KEY_2

· If setting mode has not been exited, you can change the camera standard by pressing KEY2 circularly.

· The LED_NAME indicator will blink all the time until exit out the setting mode.

· If without any operation in 10 seconds, it will exit out setting mode automatically.

· In this step,press KEY_SET button three times to exit out the setting mode manually.

Setting Prompt Voice

Max. 9-languages voice to select, No voice, Voice 1 and Voice 2 ...

Voice 1 is default, to change the setting, please follow the steps:

In standby mode, press

KEY_SET button twice.

UNLOCK Indicator:OFF

CALL Indicator:ON

Press KEY_3 button to set the

prompt voice to Voice 1.

UNLOCK Indicator:OFF

CALL Indicator:ON

Press KEY_3 button again

to set the prompt voice to

Voice 2.

UNLOCK Indicator:OFF

CALL Indicator:ON

Press KEY_3 button again

and again to set the prompt

voice to No voice.

UNLOCK Indicator:OFF

CALL Indicator:ON

Buzzer

Beep+, Beep

Buzzer

Play the voice 1

Buzzer

Play the voice 2

Buzzer

Beep+

Press KEY_3

· If setting mode has not been exited, you can change the prompt voice by pressing KEY3 circularly.

· The LED_NAME indicator will blink all the time until exit out the setting mode.

· If without any operation in 10 seconds, it will exit out setting mode automatically.

· The voice can be customized.

-9-

SETUP INSTRUCTIONS

Setting Prompt Voice Volume

Total 9 level can be configured. It can be modified either before or after installation.

6 is default, to change the setting, please follow the steps:

In standby mode, press

KEY_SET button twice.

UNLOCK Indicator:OFF

CALL Indicator:ON

Press KEY_4 button to set the

volume level.

UNLOCK Indicator:OFF

CALL Indicator:ON

Press KEY_4 button again

and again to set the volume

level you want.

UNLOCK Indicator:OFF

CALL Indicator:ON

Buzzer

Beep+, Beep

Buzzer

Play the volume

Buzzer

Play the volume level 9

Press KEY_4

· If setting mode has not been exited, you can change the volume level by pressing KEY4 circularly.

· The LED_NAME indicator will blink all the time until exit out the setting mode.

· If without any operation in 10 seconds, it will exit out setting mode automatically.

Setting Unlock Mode

There are 2 unlock modes, Normally opened and Normally closed.

Normally opened is default, to change the setting, please follow the steps:

In standby mode, press

KEY_SET button three

times.

UNLOCK Indicator:ON

CALL Indicator:OFF

Press KEY_1 button to set

the unlock mode to

Normally opened.

UNLOCK Indicator:ON

CALL Indicator:OFF

Press KEY_1 button again

to set the unlock mode to

Normally closed.

UNLOCK Indicator:ON

CALL Indicator:OFF

Buzzer

Beep+, Beep

Buzzer

Beep+

Buzzer

Beep, Beep

Press KEY_1

· If setting mode has not been exited, you can change the unlock mode by pressing KEY1 circularly.

· The LED_NAME indicator will blink all the time until exit out the setting mode.

· If without any operation in 10 seconds, it will exit out setting mode automatically.

· In this step,press KEY_SET button twice to exit out the setting mode manually.

-10-

SETUP INSTRUCTIONS

Setting Unlock Time

By default, the unlock time is 1s, but it can be changed,the setting range is 1s~99s.

Follow the steps:

In standby mode, press

KEY_SET button three

times.

UNLOCK Indicator:ON

CALL Indicator:OFF

Press and hold on KEY_2

button. The time you holding

on is the new unlock time.

UNLOCK Indicator:ON

CALL Indicator:OFF

Buzzer

Beep+, Beep

Buzzer

Beep,Beep......

· When entering time delayed setting, the buzzer sound one time every second.

· The LED_NAME indicator will blink all the time until exit out the setting mode.

· If without any operation in 10 seconds, it will exit out setting mode automatically.

· In this step,press KEY_SET button twice to exit out the setting mode manually.

Setting Nameplate Illumination Mode

There are 3 illumination modes for nameplate indicator, Normally on,Normally off and Auto.

Normally on is default, to change the setting, please follow the steps:

In standby mode, press

KEY_SET button three

times.

UNLOCK Indicator:ON

CALL Indicator:OFF

Press KEY_3 button to set

the nameplate illumination

mode to Normally on.

UNLOCK Indicator:ON

CALL Indicator:OFF

Press KEY_3 button again

to set the nameplate illumina-

tion mode to Normally off.

UNLOCK Indicator:ON

CALL Indicator:OFF

Press KEY_3 button again

and again to set the nameplate

illumination mode to Auto.

UNLOCK Indicator:ON

CALL Indicator:OFF

Buzzer

Beep+, Beep

Buzzer

Beep+

Buzzer

Beep, Beep

Buzzer

Beep, Beep,Beep

Press KEY_3

· If setting mode has not been exited, you can change the nameplate illumination mode by pressing KEY3

circularly.

· The LED_NAME indicator will blink all the time until exit out the setting mode.

· If without any operation in 10 seconds, it will exit out setting mode automatically.

· In this step,press KEY_SET button twice to exit out the setting mode manually.

-11-

SETUP INSTRUCTIONS

Setting Night View LED Illumination Mode

There are 3 working modes for night view LED indicator, Normally on,Normally off and Auto.

Auto is default, to change the setting, please follow the steps:

In standby mode, press

KEY_SET button three

times.

UNLOCK Indicator:ON

CALL Indicator:OFF

Press KEY_4 button to set

the night view LED mode

to Normally on.

UNLOCK Indicator:ON

CALL Indicator:OFF

Press KEY_4 button again

to set the night view LED

mode to Normally off.

UNLOCK Indicator:ON

CALL Indicator:OFF

Press KEY_4 button again

and again to set the night

view LED mode to Auto.

UNLOCK Indicator:ON

CALL Indicator:OFF

Buzzer

Beep+, Beep

Buzzer

Beep+

Buzzer

Beep, Beep

Buzzer

Beep, Beep,Beep

Press KEY_4

· If setting mode has not been exited, you can change the night view LED illumination mode by pressing

KEY4 circularly.

· The LED_NAME indicator will blink all the time until exit out the setting mode.

· If without any operation in 10 seconds, it will exit out setting mode automatically.

· In this step,press KEY_SET button twice to exit out the setting mode manually.

Setting Ring-back Tone

If allow ring-back tone, press the call button to call monitor, a ring-back call tone can be heard

from door station.

There are 3 ring-back call tones, Ringing one time, Ringing continuously and No ring-back

tone.

Ringing one time is default, to change the setting, please follow the steps:

In standby mode, press

KEY_SET button four

times.

UNLOCK Indicator:ON

CALL Indicator:ON

Press KEY_1 button to set

the ring-back call tone ringing

one time.

UNLOCK Indicator:ON

CALL Indicator:ON

Press KEY_1 button again

to set the ring-back call tone

ringing continuously.

UNLOCK Indicator:ON

CALL Indicator:ON

Press KEY_1 button again

and again to close ring-back

call tone.

UNLOCK Indicator:ON

CALL Indicator:ON

Buzzer

Beep+, Beep

Buzzer

Beep+

Buzzer

Beep, Beep

Buzzer

Beep, Beep,Beep

Press KEY_1

· If setting mode has not been exited, you can change the ring-back tone by pressing KEY1 circularly.

· The LED_NAME indicator will blink all the time until exit out the setting mode.

· If without any operation in 10 seconds, it will exit out setting mode automatically.

· In this step,press KEY_SET button once to exit out the setting mode manually.

-12-

SETUP INSTRUCTIONS

Setting Image Display Mode

Please know that this setting is only effective for monitors which does not support man-

ual operation for pan-tilt.

When the monitor being called

When door station calls monitor,the image will be displayed on screen,there are 3 modes for im-

age displayed, Alternate switching mode,Zoom mode and Full screen mode.

Alternate switching mode: when the monitor being called, switch at regular time(5s) between

Full screen and Zoom image.

Zoom mode: when the monitor being called, the image will be displayed on full screen for 5

seconds, then switch to Zoom image.

Full screen mode: when the monitor being called, the image will be always displayed on Full

screen.

Alternate switching mode is default, to change the setting, please follow the steps:

In standby mode, press

KEY_SET button four

times.

UNLOCK Indicator:ON

CALL Indicator:ON

Press KEY_2 button to set

the image display mode

to Cycle switching.

UNLOCK Indicator:ON

CALL Indicator:ON

Press KEY_2 button again

to set the image display

mode to Zoom mode.

UNLOCK Indicator:ON

CALL Indicator:ON

Press KEY_2 button again

and again to set the image

display mode to Full screen.

UNLOCK Indicator:ON

CALL Indicator:ON

Buzzer

Beep+, Beep

Buzzer

Beep+

Buzzer

Beep, Beep

Buzzer

Beep, Beep,Beep

Press KEY_2

en mode in cycle.

· If setting mode has not been exited, you can change the image display mode by pressing KEY2 circularly.

· The LED_NAME indicator will blink all the time until exit out the setting mode.

· If without any operation in 10 seconds, it will exit out setting mode automatically.

· In this step,press KEY_SET button once to exit out the setting mode manually.

When answering the call

When answering the call, the image switching reminder can be activated or forbidden.

If set to activated mode, the image switching reminder will be different for different image display

mode.

Alternate switching mode: When answering the call, image switching reminder is not effective.

Zoom mode: When answering the call, the image will be displayed on full screen for 5 sec-

onds, then switch to Zoom image to remind to enter talking status.

-13-

SETUP INSTRUCTIONS

Full screen mode: When answering the call, the image will be displayed on Zoom mode for 5

seconds, then switch to Full screen to remind to enter talking status.

If set to forbidden mode, there is no image switching reminder at any image display mode.

Activated is default, to change the setting, please follow the steps:

In standby mode, press

KEY_SET button four

times.

UNLOCK Indicator:ON

CALL Indicator:ON

Press KEY_3 button to

activate image switching

when answering the call.

UNLOCK Indicator:ON

CALL Indicator:ON

Press KEY_3 button again

to forbid image switching

when answering the call.

UNLOCK Indicator:ON

CALL Indicator:ON

Buzzer

Beep+, Beep

Buzzer

Beep+

Buzzer

Beep, Beep

Press KEY_3

· If setting mode has not been exited, you can change the image display mode by pressing KEY3 circularly.

· The LED_NAME indicator will blink all the time until exit out the setting mode.

· If without any operation in 10 seconds, it will exit out setting mode automatically.

· In this step,press KEY_SET button once to exit out the setting mode manually.

RAINY_COVER Configure

If can be set the rainy cover mode.

Mounting the rainy cover is default, to change the setting, please follow the steps:

In standby mode, press

KEY_SET button four

times.

UNLOCK Indicator:ON

CALL Indicator:ON

Press KEY_4 button to set

the rainy cover mode.

UNLOCK Indicator:ON

CALL Indicator:ON

Press KEY_4 button again

to set the no rainy cover

mode.

UNLOCK Indicator:ON

CALL Indicator:ON

Buzzer

Beep+, Beep

Buzzer

Beep+

Buzzer

Beep, Beep

Press KEY_4

· If setting mode has not been exited, you can change rainy cover mode by pressing KEY4 circularly.

· The LED_NAME indicator will blink all the time until exit out the setting mode.

· If without any operation in 10 seconds, it will exit out setting mode automatically.

· In this step,press KEY_SET button once to exit out the setting mode manually.

-14-

SETUP INSTRUCTIONS

Registering ID Card

· Up to 320 user cards can be registered by the door station.

· Easy management with LED status and sound hints.

· There are two master cards, one MASTER CARD ADD card

and one MASTER CARD DELETE card, When registered new

master cards, the old master cards are invalid automatically.

· Card reading distance is less than 3cm.

· The master cards are necessary when you add or delete user

cards. Please keep it well for future use.

· EM card, 125kHz.

Authorizing master cards:

By default,there are two master cards marked MASTER CARD ADD and MASTER CARD

DELETE ,but you should know that the master card can be authorized by users at any time.

That means any two user cards can be authorized to master cards,When registered new master

cards, the old master cards will be invalid automatically.

When power on in 10s,press

and hold on KEY_SET button

for 3s.

UNLOCK Indicator:OFF

CALL Indicator:OFF

Press KEY_2 button.

UNLOCK Indicator:Blink one time

CALL Indicator:OFF

Show the first card to ID

card window, set the card

of MASTER CARD ADD.

UNLOCK Indicator:Blink two times

CALL Indicator:OFF

Show the second card to ID

card window, set the card of

MASTER CARD DELETE.

UNLOCK Indicator:Blink three times

CALL Indicator:OFF

Buzzer

Beep+, Beep

Buzzer

Beep+

Buzzer

Beep,Beep

Buzzer

Beep,Beep,Beep

· The LED_NAME indicator will blink twice per second until exit out the master card authorized mode.

· If without any operation in 10 seconds, it will exit out setting mode automatically.

· It will exit out setting mode automatically after showing these two cards,the UNLOCK&CALL indicator will be

turned off.

-15-

SETUP INSTRUCTIONS

Switching Access Control:

The access can be controlled by door station or DT-ACC,so it’s available to switch the access

function.

Show the master card of

MASTER CARD DELETE

again to switch as a door

station access control.

UNLOCK Indicator:OFF

CALL Indicator:OFF

Show the master card of

MASTER CARD ADD to ID

card window in standby.

UNLOCK Indicator:OFF

CALL Indicator:ON

Show the master card of

MASTER CARD DELETE

to ID card window.

UNLOCK Indicator:ON

CALL Indicator:ON

Buzzer

Beep+

Buzzer

Beep+, Beep

Buzzer

Beep+, Beep

Show the master card of

MASTER CARD DELETE

again to switch to DT-ACC

controlled.

UNLOCK Indicator:OFF

CALL Indicator:OFF

Buzzer

Beep,Beep

· If without any operation in 10 seconds, it will exit out setting mode automatically.

· If current access is controlled by door station, next access switching setting is controlled by DT-ACC.

Adding User Cards:

Show the master card of

MASTER CARD ADD to ID

card window in standby.

UNLOCK Indicator:OFF

CALL Indicator:ON

Show user cards to be

added in sequence.

UNLOCK Indicator:OFF

CALL Indicator:Blink one time

Show the master card of

MASTER CARD ADD again

to exit.

UNLOCK Indicator:OFF

CALL Indicator:OFF

Buzzer

Beep+, Beep

Buzzer

Beep+

Buzzer

Beep, Beep+

· If without any operation in 10 seconds, it will exit out setting mode automatically.

· To add user card, the access must be controlled by door station.

-16-

SETUP INSTRUCTIONS

Deleting User Cards:

Show the master card of

MASTER CARD DELETE to

ID card window in standby.

UNLOCK Indicator:ON

CALL Indicator:OFF

Show user cards to be

deleted in sequence.

UNLOCK Indicator:Blink one time

CALL Indicator:OFF

Show the master card of

MASTER CARD DELETE

again to exit.

UNLOCK Indicator:OFF

CALL Indicator:OFF

Buzzer

Beep+, Beep

Buzzer

Beep+

Buzzer

Beep, Beep+

· .If without any operation in 10 seconds, it will exit out setting mode automatically.

· To add user card, the access must be controlled by door station.

Initializing Access (delete all user cards):

Show the master card of

MASTER CARD DELETE to

ID card window in standby.

UNLOCK Indicator:ON

CALL Indicator:OFF

Show the master card of

MASTER CARD ADD to ID

card window.

UNLOCK Indicator:ON

CALL Indicator:ON

Show the master card of

MASTER CARD ADD again,

format is activated.

UNLOCK Indicator:Blink for some time

CALL Indicator:Blink for some time

Buzzer

Beep+, Beep

Buzzer

Beep+, Beep

Buzzer

Beep

· If without any operation in 10 seconds, it will exit out setting mode automatically.

· To add user card, the access must be controlled by door station.

· At step3, the UNLOCK & CALL indicator will blink all time until formatting is finished.

· When formatting is finished, UNLOCK & CALL indicator will be turned off and sound “ Beep+ ”, and exit out

setting mode automatically.

Restore To Default

The restore to default function allows the user to recover the settings to factory setting.

When power on in 10s,press

and hold on KEY_SET button

for 3s.

UNLOCK Indicator:OFF

CALL Indicator:ON

Press KEY_3 button.

UNLOCK Indicator:ON

CALL Indicator:ON

Buzzer

Beep+, Beep

Buzzer

Beep+

· The LED_NAME indicator will blink twice per second until exit out the restore to default mode.

· If without any operation in 10 seconds, it will exit out setting mode automatically.

· When restoring is finished, UNLOCK & CALL indicator will be turned off, and exit out setting mode

automatically.

-17-

WIRING

Connecting Electric Lock

Door Lock Controlled with Internal Power

1.Electronic lock of Power-on-to-unlock

type should be used.

2.The door lock is limited to 12V, and hold-

1 2 3

Jumper position on 2&3

ing current must be less than 250mA.

L1

L2

PL

S+

S-

3.The jumper should be placed on position

2 and 3 before connecting.

4.The door lock control is not timed from

Exit Button(EB).

5.The Unlock Mode must be set to 0 (by

default).

Door Lock Controlled with Dry Contact

1.The external power supply must be used

according to the lock.

2.The inside relay contact is restricted to

230Vac 1A or 24Vdc 1A.

* EB

1 2 3

Take off the jumper

LOCK

3.The jumper must be taken off before

connecting.

L1

L2

PL

S+

S-

4.Setup the Unlock Mode according to

different lock types.

· Power-on-to-unlock type:Unlock

Mode=0 (by default)

· Power-off-to-unlock type:Unlock

Mode=1

* DT-RLC relay actuator is needed for 2nd lock connection.

-18-

POWER

SUPPLY

LOCK

WIRING

As The Villa System Door Stations

1st door station

ID=0

RFCARD

L1 L2 PL S+ S-

2nd door station

ID=1

RFCARD

L1 L2 PL S+ S-

3rd door station

ID=2

RFCARD

L1 L2 PL S+ S-

AC~

100~240VAC

PC6A

A B C D

DBC4A1

4th door station

ID=3

RFCARD

L1 L2 PL S+ S-

Impedance

switch

OFF

ON

BUS(IM) BUS(DS)

Code=31，DIP6=on

Code=30，DIP6=off

Code=0，DIP6=off

· Door stations were configured as the villa system door stations.

· Max.4 door stations can be connected to the system.

· Ensure to set the correct address for each door station, Refer to Page 8 for more details

about the address setting of door stations.

-19-

WIRING

As The Apartment System Door Stations

Common

Door Station

RFCARD

AC~

A B C D

LAN Switcher

Guard Unit

IPG

BUS(DS)BUS(IM)

AC~

PC6A

PC6A

BUS(IM)BUS(DS)

DBC4A1

BUS(IM)BUS(DS)

2 Wire cable

CAT5 cable

RFCARD

IPG

BUS(DS)BUS(IM)

AC~

PC6A

BUS(IM)BUS(DS)

· Door stations were configured as the apartment system door stations.

· The door station is also compatible with other monitors which are provided by our company.

-20-

APPENDIX

Precautions

· Please clean the unit with soft cotton cloth, don't use the organic impregnant or chemical

clean agent. If necessary, please use a little pure water or dilute soap water to clean the dust.

· The unit is weather resistant. However do not spray high pressure water on access control

keypad directly. Excessive moisture may cause problems with the unit.

· You must use the right adaptor which is supplied by the manufacture or approved by the

manufacture.

· Pay attention to the high voltage inside the products, please refer service only to a trained

and qualified professional.

Specification

● Power Supply :

● Power Consumption:

● Fish Camera:

●

● 3089 Camera:

●

● Lock Power supply:

● Unlock time:

● Number of relay circuits:

●

● Working temperature:

● Wiring:

● Protection:

● Dimension:

DC 24V;

Standby 1.2W; Working status 4.8W;

Color CMOS, 2.0 Mega pixel 1/2.7’’

fisheye camera,170° wide angle(DT608);

Color CMOS, 520TVL , 1/4’’ camera,

1050 wide angle (DT608C)；

12Vdc, 250mA(Internal Power);

1~99s(Default 1s);

2 (the second lock need external

device to support);

-20ºC ~ +55ºC;

2 wires,non-polarity;

IP45;

281(H)×110(W)×44(D)mm.

-21-

APPENDIX

Cables and Requirments

The maximum distance of the wiring is limited in the DT system. Using different cables may also

affect the maximum distance which the system can reach.

Basic IN-OUT Wiring Mode

Cable and distance(unit:m)

Cable Usage

Twisted cable 2x0.75mm2

A

60

B

≤2 IM

100

B

≤16 IM

40

B

Twisted cable 2x1mm2

80

120

60

PC6A

A

RFCARD

-22-

APPENDIX

Star Topology Wiring Mode With DBC4A1

2

DBC4A1

B

2

C

PC6A

Cable and distance(unit:m)

A

RF CARD

| -23-Cable Usage | A | B | C |
| --- | --- | --- | --- |
| 2 Twisted cable 2x0.75mm | 60 | 60 | 30 |
| 2 Twisted cable 2x1mm | 80 | 80 | 40 |

DT-ENG-608-V1

The design and specifications can be changed without notice to the user. Right to interpret and copyright of this

manual are preserved.