DT-DBC4A1 USER MANUAL

V1.0

20151107

Description: DBC4A1 video distributor with 4 branches and isolation protection

function.

·  Can be used as 4 inputs(outdoor stations) controller or 4 outputs(indoor stations)

controller;

·  Separate isolation protection without affecting another devices on bus system;

·  Short-circuit indication for convenient maintenance;

·  Periodic self-detection mechanism for recovery.

1. Parts and Functions

Impedance

OFF

ON

POWER

DBC4A1

IN-USE

Output

Output

BUS

A

B

C

D

IN-USE:Status indicator,it will light up when receives signal.

POWER:Working indicator,it will light up when plugs in power supply.

Impedance Switch:Video match switch,the last DBC4A1 at the end of the

bus should set ON to match the video impedance,the

power indicator will turn to orange after setting.

Bus:Input port,bus connection port.

A,B,C,D:Output port,connect to indoor monitors or door stations.

Note:

·  Operation mode: Protection mode will be activated once its connected devices

are short circuited, and power supply for ABCD outputs will be turn off, the

flashing in-use indicator shows the distributor is in the protection mode.

·  Self-detection: System will auto check whether the short circuit is fixed or not,

then recover the power supply, and in-user indication will be turn off;

·  Detection period: Self-detection will be happened regularly according rules, and

in-use indicator will flash rapidly three times when check happens;

1st detection will be happened in 10 seconds after short circuit;

-1-switch

2nd detection will be happened in 60 seconds after 1st detection;

3rd detection will be happened in 5 minutes after 2nd detection;

4th detection will be happened in 10 minutes after 3rd detection;

5th hereafter detection will be happened every 30 minutes;

2. Unit Mounting

DBC4A1

DIN Rail Mounting

3. System Wiring with DBC4A1

Mulit Door Station Wiring:

4# Camer    a

ID=11

ON

3# Camer    a

ID=01

ON

2# Camer    a

ID=10

ON

1# Camer    a

ID=00

ON

L1 L2 PL S1+ S2+ S-

12

L1 L2 PL S1+ S2+ S-

1 2

L1 L2 PL S1+ S2+ S-

1 2

L1 L2 PL S1+ S2+ S-

1 2

monitors

AC~

100~240VAC

A B C D

DBC4A1

PC6

OFF

BUS(IM) BUS(DS)

ON

Impedance

switch

Note:DBC4A1 applies to all door station and monitor, the diagram uses DT591 as an

example.

-2-12

12

ON

ON

12

12

ON

ON

Mulit Monitors Wiring:

ON

monitor

1 2 3 4 5 6

monitor

Code=15, DIP-6=on

Code=14, DIP-6=on

Impedance

switch

OFF ON

ON

monitor

1 2 3 4 5 6

monitor

Code=13, DIP-6=on

monitor

Code=12, DIP-6=on

monitor

Code=3, DIP-6=on

Code=2, DIP-6=on

Impedance

switch

OFF ON

ON

Code=1, DIP-6=on

monitor

1 2 3 4 5 6

Code=0, DIP-6=on

monitor

AC~

100~240VAC

PC6

BUS(IM) BUS(DS)

ID=00

ON

1 2

| -3-ON |  |  |  |  |
| --- | --- | --- | --- | --- |
| 1 2 | 3 | 4 | 5 | 6 |

| ON |  |  |  |  |
| --- | --- | --- | --- | --- |
| 1 2 | 3 | 4 | 5 | 6 |

| ON |  |  |  |  |
| --- | --- | --- | --- | --- |
| 1 2 | 3 | 4 | 5 | 6 |

| ON |  |  |  |
| --- | --- | --- | --- |
| 1 2 | 3 | 4 5 | 6 |

| ON |  |  |  |  |
| --- | --- | --- | --- | --- |
| 1 2 | 3 | 4 | 5 | 6 |

A B C D

A B C D

DBC4A1

DBC4A1

5. Specification

Power Supply :

DC20~30V

Working Temperature:

-100C~+400C;

Wiring:

Dimension:

2 wires (non-polarity);

89(H)×71(W)×45(D)mm

The design and specifications can be changed without notice to the user. Right to interpret

and copyright of this manual are preserved.

DT-ENG-DBC4A1-V1      20151107