DT-DBC4R

Riser Distributor

User Manual

DBC4R

POWER

IN-USE

Please read this manual carefully before using the product you purchase, and keep it well for

future use.We reserve the right to modify the specification in this manual at any time without

notice.

1. Description

The DBC4R is a 4 output video amplifier.

· There are 2 working modes: riser mode and distributor mode;

· Separate isolation protection without affecting another devices on bus system;

· Short-circuit indication for convenient maintenance;

· Periodic self-detection mechanism for recovery.

2. Parts and Functions

1

ON

Impedance

switch

OFF

DBC4R

DIP Switch

2

3

ON

POWER IN-USE

Output

Output

BUS

A

B

C

D

IN-USE

Status indicator

POWER Video match indicator

Standby: off

Device working: on

not match: red

match: orange

Power protection: slow flash

Device search mode: fast flash

Impedance Switch: Video match switch.

Bus: Input port,bus connection port.

A,B,C,D: Output port,connect to indoor monitors.

-2-

DIP Switch: 3 bit DIP switches,about the DIP settings,see follows:

ON

OFF

DIP1

DIP2

DIP3

the unit work in riser mode

the unit start to search the

local monitors (for monitors

with built-in power)

Gain High

the unit work in distributor mode

the unit stop to search the

monitors (in normal use)

Gain Auto

Note:

· Operation mode: Protection mode will be activated once its connected devices are

short circuited, and power supply for ABCD outputs will be turn off, the flashing in-

use indicator shows the distributor is in the protection mode.

· Self-detection: System will auto check whether the short circuit is fixed or not, then

recover the power supply, and in-user indication will be turn off;

· Detection period: Self-detection will be happened regularly according rules, and in-

use indicator will flash rapidly three times when check happens;

1st detection will be happened in 10 seconds after short circuit;

2nd detection will be happened in 60 seconds after 1st detection;

3rd detection will be happened in 5 minutes after 2nd detection;

4th detection will be happened in 10 minutes after 3rd detection;

5th hereafter detection will be happened every 30 minutes;

3. Unit Mounting

DBC4R

DIN Rail Mounting

-3-

4. System Wiring with DBC4R

1.Basic IN-OUT expansion wiring(distributor mode)

A

PC6A

4R

B

4R

DBC4R

Wiring diagram:

Max.4

AC~

100~240VAC

PC6A

BUS(IM) BUS(DS)

DBC4R

1

ON

2

3

DIP1->OFF

* Max.8 monitors can be connected for every DBC4R.

| -4-Cable Usage | A | B |
| --- | --- | --- |
| 2 Twisted cable 2x0.75 mm | 75 | 65 |
| 2 Twisted cable 2x1.00 mm | 80 | 70 |

A B C D

DBC4R

2.Multi risers wiring(riser mode)

Type 1

C

Max.8

4R

4R

4R

DBC4R

B

4

4

1

2

3

PC6A 4R

4

7

*

5

8

0

6

9

#

A

Max.4 risers

| -5-Cable Usage | A | B | C |
| --- | --- | --- | --- |
| 2 Twisted cable 2x0.75 mm | 75 | 65 | 30 |
| 2 Twisted cable 2x1.00 mm | 80 | 70 | 35 |

A

A

4RA

4RA

Wiring diagram:

A B C D

DBC4R

to next branch distributor

Max.4 risers

AC~

100~240VAC

A B C D

DBC4R

to next branch distributor

1

ON

A B C D

2

3

DIP1->ON

DBC4R

PC6A

BUS(IM) BUS(DS)

Wiring diagram:

1

4

7

*

2

5

8

0

3

6

9

#

A B C D

DBC4R

to next branch distributor

AC~

100~240VAC

A B C D

DBC4R

to next branch distributor

1

ON

A B C D

A B C D

2

3

DIP1->ON

DBC4R

DBC4R

PC6A

BUS(IM) BUS(DS)

to next DBC4R

1

4

7

*

2

5

8

0

3

6

9

#

* The DIP1 should set to “ON” for all DBC4R.

-6-

3.Multi monitors wiring(distributor mode)

4R

4R

4R

1

4

2

5

3

6

PC6A

7

*

8

0

9

#

4R

DBC4R

Wiring diagram:

OFF ON

1

2

3

ON

* The impedance switch

should set to “ON” for

the last DBC4R at the

end of the bus.

Impedance

switch->ON

DIP1->OFF

OFF ON

1

2

3

ON

Impedance

switch->OFF

DIP1->OFF

AC~

100~240VAC

PC6A

BUS(IM) BUS(DS)

1

4

7

*

2

5

8

0

3

6

9

#

-7-A B C D

A B C D

DBC4R

DBC4R

5. Specification

Power Supply :

Working Temperature:

Wiring:

Dimension:

Standby Current:

DC20~30V

-100C~+400C

2 wires (non-polarity)

89(H)×71(W)×45(D)mm

4~5mA

The design and specifications can be changed without notice to the user. Right to interpret and

copyright of this manual are preserved.

DT-ENG-DBC4R-V1

20190509